## Slide 1
SoLID DAQ test stand status
Hanjie Liu
Data acquisition working group
University of Massachusetts - Amherst
Data Acquisition
Jefferson Lab SoLID Pre-R&D Review
August 7th, 2020

## Slide 2: Outline
UMASS test stand setup and goals
Compton setup and performance
Conclusion

## Slide 3: Work Plan
UMASS DAQ stand

## Slide 4: UMASS test stand setup Test the performance of the FADC fast readout thought the VXS backplane in terms of deadtime and rate capabilities Develop FADC based calorimeter trigger for PVDIS Test the PVDIS trigger consisting of a coincidence between the Cherenkov and Calrimeter trigger Study effect of dead time on measurement of full system FADC + GEM Check pedestal width and ability to measure asymmetries at the ppm level required for PVDIS
TI
SD
FADC
VTP
VETROC
PVDIS: ECal, Cherenkov FADC
SIDIS: ECal FADC;
MRPC VETROC
GEM interface board
Goal of the test stand
Helicity board
TO BE DONE

## Slide 5
Compton DAQ setup during CREX
FADC
photon calorimeter signal, helicity
electron detector strip timing
BCM, Cavity power
trigger from VTP, MPS
VTP (VXS-Trigger-Processor) get all the front-end boards information through the VXS crate. FPGA program trigger
generate trigger
generate trigger
record past helicity information
VETROC scaler and trigger scaler
VETROC
SCALER
TI
VTP
DONE

## Slide 6: Test during CREX in Compton test stand
Deployed FADC for Compton photon detector and VETROC for electron detector
Developed helicity scalers for normalization and dead time correction
Implemented delayed helicity recording
Developed basic software for analysis of asymmetries and dead time
Starting observing Compton asymmetries
DONE

## Slide 7: Deadtime
 | T1 dead time | error | T3 dead time | error
laser on, beam>130 uA | 9.49% | 0.004% | 38.2% | 0.07%
laser off, beam>130 uA | 9.06% | 0.005% | 35.1% | 0.2%
beam off | 8.77% | 0.008% | 17.2% | 3.6%
T1: at least two e planes
T3: photon (prescale =1000) block level=20

## Slide 8: Preliminary results
Compton asymmetry ( expected asymmetry around 6% at maximum )
Asymmetry changes sign with half wave plate as expected
Start of optimization for maximum trigger rate ( around 50 KHz )
Some features still need to be understood ( under study ) some physics related other might be electronics related

## Slide 9: Conclusion
Delayed helicity scheme implemented and software developed to handle it
Deployed system for Compton Polarimetry : physics asymmetry could be observed
Fast FADC readout being developed
Umass test stand being put together
Expect a few months shift from initial schedule but will finish before expected end of project